Analog IC Design
Lecture 2 circuits and systems review

---
Laplace Transform (LT)
L
L
H(s)

---
Laplace Transform (LT)
Laplace transform helps you to solve differential equations by multiplication and division
H(s)
Y(s)
U(s)
Y(S)=H(s)U(s)

---
Laplace Transform (LT)

---
Poles and Zeros
- Transfer function
- Zeros:roots of the numerator N(s) = 0
- Poles: roots of the denominator (characteristic eq.) D(s) =0
- For physical systems, poles & zeros are real or complex conjugate
  Notes:
  - If the system input is impulse in the time domain then the output is the transfer function in laplace domain

---
Real and Complex Poles

---
LHP and RHP Poles
- Poles in LHP: Decaying exponential (stable system)
- Poles in RHP: Growing exponential (unstable system)

---
First-Order LPF
- 𝜏 = 𝑅𝐶: time constant
@ w = infinity

---
First-Order LPF Bode Plot

---
First-Order HPF

---
First-Order HPF Bode Plot

---
Second-Order System: LC LPF

---
Second-Order Passive LC LPF

---
Second-Order System Poles

---
Ringing and Peaking
Q < 0.5 (ζ > 1) over damped system roots are real,
negative, and distinct
1. Q = 0.5 (ζ = 1):critical damped system, roots are
  real, negative, and equal
2. Q > 0.5 (ζ < 1):under damped system,roots are
  complex conjugate
  Problems:
        - Increase settling time
        - Overshoot and undershooting which is calculated by

---
Ringing and Peaking
Ringing at time happens first at Q > 0.5 then peaking at frequency domain at Q > 0.707